## Slide 1
DIGITAL DESIGN & COMPUTER ARCHITECTURE
MULTI-BIT BINARY ADDER & SUBTRACTOR
A 4-bit arithmetic circuit using full adders, XOR gates and mode control
TEAM MEMBERS
Bhuvana | 2620030052
M. Harshithaa Reddyy | 2620030118
Nishitha | 2620030113
Sai Kiran | 2620030061
OPERATION SELECT
M = 0 ADD
M = 1 SUBTRACT
A + B / A − B
SECTION: __________ SUBJECT: DDCA
FINAL PROJECT DEMONSTRATION

## Slide 2
DDCA / 02
Introduction & Objective
One circuit. Two arithmetic operations.
WHY BINARY ARITHMETIC?
•
Digital systems represent data using 0s and 1s.
•
Arithmetic circuits are used inside processors and ALUs.
•
A shared design performs addition and subtraction.
PROJECT OBJECTIVE
Design and simulate a 4-bit circuit that adds or subtracts two binary inputs.
M = 0 A + B
M = 1 A − B
Outputs: S3–S0 (4-bit result) and final carry-out.

## Slide 3
DDCA / 03
Theory & Logic Circuit
XOR gates conditionally invert B; full adders calculate the result.
ADDITION MODE
M = 0 → B′ = B, C₀ = 0
SUBTRACTION MODE
M = 1 → B′ = NOT B, C₀ = 1
B′ = B XOR M C₀ = M
4-BIT RIPPLE-CARRY ADDER–SUBTRACTOR
M
XOR 3
FULL ADDER 3
S3
A3, B3
C2
XOR 2
FULL ADDER 2
S2
A2, B2
C1
XOR 1
FULL ADDER 1
S1
A1, B1
C0
XOR 0
FULL ADDER 0
S0
A0, B0
Four full adders are linked by carry signals. M controls all XOR gates and C₀.

## Slide 4
DDCA / 04
Circuit Design in Logisim
Use this schematic as a guide; replace it with your actual Logisim screenshot before submission.
LOGIC CIRCUIT OVERVIEW (ILLUSTRATION)

## Slide 5
DDCA / 05
Simulation Results
Expected test cases — verify in Logisim and insert real screenshots.
TEST 1 / ADDITION
A = 0101 B = 0011 M = 0
Expected result: 1000 (5 + 3 = 8)
TEST 2 / SUBTRACTION
A = 0111 B = 0011 M = 1
Expected result: 0100 (7 − 3 = 4)
RESULTS TABLE
Test
A
B
M / Mode
Expected
Observed
1
0101
0011
0 / Add
1000
Fill after test
2
0111
0011
1 / Sub
0100
Fill after test
Do not label expected values as observed results until you have tested the circuit.

## Slide 6
DDCA / 06
Conclusion & Applications
A compact arithmetic building block for digital systems.
KEY TAKEAWAYS
•
One circuit supports addition and subtraction.
•
XOR gates and mode control enable two’s-complement subtraction.
•
Ripple-carry designs are simple but can have propagation delay.
•
Possible improvement: a carry-lookahead design.
APPLICATIONS
ALUs
Arithmetic in processors
Calculators
Basic binary operations
Embedded systems
Digital control and computation
THANK YOU